#### Using the Nokia E51 as a 3G USB Modem with Windows XP

The Nokia PC Suite software (available at www.nokia.com.sg) which provides the modem drivers needs to be installed first BEFORE connecting.

After the software is installed, connect the phone to the PC.

The phone will prompt you whether you want to connect in PC Suite mode or Data Transfer mode. Select PC Suite mode.

Go to Control Panel -> for Phone and Modem Options. Click on the Modems tab, a list of available modems will be displayed:

Select the Nokia modem from the list and click on the Properties button.

Click on the Advanced tab and key in the following in the field:

In the Extra Initialisation Commands field, enter the following string (select the appropriate access point for your network provider):

M1 Singapore: at+cgdcont=1,”IP”,”sunsurf”

Vodafone: at+cgdcont=1,"IP","internet"

Orange: at+cgdcont=1,"IP","orangeinternet"

O2: at+cgdcont=1,"IP","mobile.o2.co.uk"

T-Mobile: at+cgdcont=1,"IP","general.t-mobile.uk"

Three: at+cgdcont=1,"IP","three.co.uk"

So, for example, setting up a connection to Vodafone would require the following string:

Once the setting has been entered, click OK and then OK again to return to the Control Panel.

In the Control Panel, double click the icon for Network Connections.

Select the option to Create A New Connection, the following window will be displayed:

Click Next. You will be prompted to specify the type of connection you wish to create, select the option to Connect To The Internet:

Click Next. Select the option to Set Up My Connection Manually:

Click Next. Select the option to Connect Using A Dial-Up Modem:

Click Next. Enter a name for the connection, 'Vodafone 3G', for example:

Click Next. You will be prompted to enter a telephone number to dial. In this field you need to enter *99#

Click Next. You will be prompted to enter a username and password for the connection.

Enter the appropriate details for your network provider:

M1 Singapore: leave blank. (Bearer settings in phone already set as “+65” for user name, “user123” for password)

Vodafone: 'web' for both

Orange: leave blank

O2: 'web for both'

T-Mobile: leave blank

Three: leave blank

When the correct settings have been entered, click Next and then click Finish. You will then be prompted to initiate the connection. Leave username and password blank if the above settings did not require any.

Click Dial. Provided all of the settings were entered correctly, after a few moments you will be connected to the Internet:

To initiate the connection at any other time, simply double click the icon in the Network Connections folder:

<< THE END >>